## Slide 1
Hadi Salimi
Distributed Systems Lab,
School of Computer Engineering,
Iran University of Science and Technology,
hsalimi@iust.ac.ir
Fall 2010
Performance Profiling in a Virtualized Environments

## Slide 2: Outline
Review of Virtualization Technology
Profiling in a Virtualized Environments
Review of Performance Profiling
Structure of a Profiler
Profiling Techniques in a Virtualized Environment
Profiling Packet Receive
Other Important Things
Conclusions

## Slide 3: Review of Virtualization Technology
Virtualization is the most Important Technology for Cloud Computing
Virtualization uses workload consolidation and migration for improves the resource utilization and the scalability of a cloud
The Virtual Machine Monitor (VMM) exports a set of virtual machines to the guest operating systems and manages accesses to the underlying hardware resources shared by multiple guests

## Slide 4: Review of Virtualization Technology(cont’d)
Diverse implementations
  Software: Xen, KVM, VMware,….
  Hardware: Intel x86, AMD x86, PowerPC,…
Opportunities for performance profiling & tuning
  Public cloud: guest OS & applications
  Private cloud: whole software stack
Profilers based on CPU performance counters do not work well with virtual machines

## Slide 5: Profiling in a Virtualized Environment
General challenge
XenOProf: profiling in the VMM
  Only for paravirtualization‐based Xen
  Require accesses to the VMM
Profiling in the guest
  Normally no results
  OProfile can't work with VMware when using performance counter interface

## Slide 6: Review of Performance Profiling
Performance Profiling = Performance evaluation
In modern processors, the Performance Monitoring Unit (PMU) is used for performance Profiling
For applications executing in a cloud, running a PMU-based profiler directly in a guest does not suitable

## Slide 7: Review of Performance Profiling (cont’d)
Understand runtime behavior
Tune performance
Mature & used extensively
  VTune, OProfile, ….
Module | Function | %CYCLE
kvm‐intel.ko | vmx_vcpu_run | 98.5529
libc.so | (no symbols) | 0.2226
vmlinux | hpet_cpuhp_notify | 0.1034
vmlinux | native_patch | 0.1034
bash | (no symbols) | 0.0557

## Slide 8: Structure of a Profiler
Performance monitoring unit (PMU)
  A Set of Performance Counters
  A Set of Event Selectors
  Generate an interrupt when a counter overflows
PMU‐based profiler
  Sampling Configuration
  Sample Collection
  Sample Interpretation

## Slide 9: Profiling Techniques in Virtualized Environment
Guest-wide Profiling
System-wide Profiling

## Slide 10: Guest-wide Profiling
Expose PMU interfaces to the guest

## Slide 11: Guest-wide Profiling (cont’d)
Where to save & restore the registers?
CPU switch
  Only in‐guest execution is accounted to the guest
Domain switch
  In‐VMM execution is also accounted to the guest

## Slide 12: Guest‐wide Profiling for KVM
Kernel‐based virtual machine (KVM)
  A Linux kernel subsystem
  A set of kernel modules + QEMU
  Built on hardware virtualization extensions
Intel VT extensions
  Provide a list of hardware features
  Facilitate our implementation
No modifications to the guest and the profiler

## Slide 13: Profiling Packet Receive
Experiment
  Push packets to a Linux guest in KVM
  Run OProfile in the guest
  Monitor instruction retirements

## Slide 14: Profiling Packet Receive (cont’d)
CPU Switch
1184 counter overflows
Module | Function | % INSTR
vmlinux | csum partial | 14.1047
vmlinux | csum partial copy generic | 8.9527
vmlinux | copy to user | 6.2500
ip tables.ko | ipt do table | 3.9696
vmlinux | tcp v4 rcv | 3.6318
libc.so | (no symbols) | 3.2095
vmlinux | ip route input | 2.8716
Vmlinux | tcp rcv established | 2.7027

## Slide 15: Profiling Packet Receive (cont’d)
Domain Switch
7286 counter overflows
Module | Function | % INSTR
8139cp.ko | cp interrupt | 31.0321
8139cp.ko | cp rx poll | 18.3365
8139cp.ko | cp start xmit | 14.1916
vmlinux | native apic mem write | 5.7782
vmlinux | native apic mem read | 5.1331
vmlinux | csum partial | 2.6215
vmlinux | csum partial copy generic | 1.4411
vmlinux | copy to user | 1.2901

## Slide 16: Other Important Things
System‐wide profiling
  Profiling in the VMM
  Provide full‐scale view: guest + VMM
Virtualization techniques
  Paravirtualization
  Dynamic binary translation
  Hardware Assistance

## Slide 17: Conclusions
Profilers do not work well with virtual machines
We implement guest‐wide profiling in a VMM based on hardware assistance
Profiling helps understand the real cost of I/O operation in a guest

## Slide 18: References
[1] Performance Counters for Linux. 2010.
http://lwn.net/Articles/310176/.
[2] G. Banga, P. Druschel, and J.C. Mogul. Resource containers: A
new facility for resource management in server systems. Operating
Systems Review, 33:45–58, 1998.
[3] P. Barham, B. Dragovic, K. Fraser, S. Hand, T. Harris, A. Ho,
R. Neugebauer, I. Pratt, and A. Warfield. Xen the art of virtualization.
In Proceedings of the nineteenth ACM symposium on
Operating systems principles, page 177. ACM, 2003

## Slide 19: References(cont’d)
[4] F. Bellard. QEMU, a fast and portable dynamic translator. In
Proceedings of the USENIX 2005 Annual Technical Conference,
FREENIX Track, pages 41–46, 2005
[5] A. Kivity, Y. Kamay, D. Laor, U. Lublin, and A. Liguori. kvm:
the Linux virtual machine monitor. In Linux Symposium, 2007.
[6] A. Menon, J.R. Santos, Y. Turner, G.J. Janakiraman, and
W. Zwaenepoel. Diagnosing performance overheads in the Xen
virtual machine environment. In VEE, volume 5, pages 13–23